## Slide 1
Tension Member
AISC Manual – 16th Edition
ANSI/AISC 360-22
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
Tension Members:
  Chapter B: Gross and Net Areas
  Chapter D: Tension Member Strength
  Chapter J: Block Shear
  Part 5: Design Charts and Tables

## Slide 3
Gross and Net Areas:
  Criteria in Section B4.3
  Strength criteria in Chapter D: Design of Members for Tension

## Slide 4
Yield on Gross Area
ft = 0.90 (Wt = 1.67)
Rupture on Effective Net Area
ft = 0.75 (Wt = 2.00)
Block Shear
ft = 0.75 (Wt = 2.00)

## Slide 5
Yield on Gross Area

## Slide 6
Pn = FyAg Equation D2-1
Yield on Gross Area
ft = 0.90 (Wt = 1.67)
Ag = Gross Area
Total cross-sectional area in the plane perpendicular to tensile stresses.

## Slide 7
Rupture on Effective Net Area

## Slide 8
Ae = Effective Net Area
Accounts for any holes or openings, potential failure planes not perpendicular to the tensile stresses, and effects of shear lag.
Pn = FuAe Equation D2-2
ft = 0.75 (Wt = 2.00)
Rupture on Effective Net Area

## Slide 9
An = Net Area = Net Width x thickness
Modify gross area (Ag) to account for the following:
Holes or openings
Potential failure planes not perpendicular to the tensile stresses.
Rupture on Effective Net Area

## Slide 10
Diagonal hole pattern:
Net Width = Gross Width + Σs2/4g – width of all holes
Section B4.3b.
s = longitudinal center-to-center spacing of holes (pitch)
g = transverse center-to-center spacing between fastener lines (gage)
g
s
Pu
Rupture on Effective Net Area

## Slide 11
Holes or openings
Section B4.3b
Use1/16” greater bolt hole width than nominal hole dimension shown in Table J3.3.
Accounts for potential damage in fabrication.
Rupture on Effective Net Area

## Slide 12
When considering angles:
Find gage (g) on page 1-52 of Manual, Table 1-7A, “Workable Gages in Angle Legs” unless otherwise noted.
Rupture on Effective Net Area

## Slide 13
An = Net Area
An = Ag- ∑(dn+1/16)t + ∑(s2/(4g))t
dn = nominal hole diameter
t = thickness of tension member
Other terms defined on previous slides
Rupture on Effective Net Area

## Slide 14
Ae = Effective Net Area
Modify net area (An) to account for shear lag.
Or value per Table D3.1
Ae = AnU Equation D3-1
U = shear lag factor reduction
= eccentricity of connection
l = length where force transfer occurs (distance parallel to applied tension force along bolts or weld)
Rupture on Effective Net Area

## Slide 15
Block Shear

## Slide 16
Block Shear
Block Shear Rupture Strength (Equation J4-5),
f = 0.75 (W = 2.00)
Agv = gross area subject to shear
Anv = net area subject to shear
Ant = net area subject to tension
Ubs = 1 or 0.5 (1 for most tension members, see Figure C-J4.2)

## Slide 17
Block Shear
Block Shear Rupture Strength (Equation J4-5),
Agv = gross area subject to shear
Anv = net area subject to shear
Ant = net area subject to tension
Ubs = 1 or 0.5 (1 for most tension members, see Figure C-J4.2)
Smaller of two values will control
ft = 0.75 (Wt = 2.00)
Notes: 17

## Slide 18
Bearing and Tear-out at Bolt Holes

## Slide 19
Bearing and Tearout at Bolt Holes
f = 0.75 (W = 2.00)
lc = clear distance, in the direction of force, between the edge of hole and the edge of adjacent hole or edge of the material.
t = thickness of connected material
d = nominal bolt diameter
Fu = specified minimum tensile strength of the connected material
    Bearing strength at each bolt
    Tearout strength at each bolt
Equation (J3-6a)
Equation (J3-6c)
These equations are for standard, oversized and short-slotted holes, independent of the direction of loading, or a long-slotted hole with the slot parallel to the direction of the bearing force when deformation at the bolt hole is a design consideration.

## Slide 20
For long-slotted holes with slot perpendicular to the direction of force:
    Bearing strength at each bolt
    Tearout strength at each bolt
Bearing and Tearout at Bolt Holes
    when deformation of the bolt hole is not a design consideration:
    Bearing strength at each bolt
    Tearout strength at each bolt
Equation (J3-6b)
Equation (J3-6d)
Equation (J3-6e)
Equation (J3-6f)

## Slide 21
Design Aids

## Slide 22
Tables 5-1 to 5-8
List available yield and rupture strength for typical sections.
Use care!
These tables assume Ae = 0.700Ag to 0.968Ag.
You must check this is met in the member and connections!
Design Aids

## Slide 23
Design Aids
Table 7-4 provides bearing strength at bolt holes based on bolt spacing.
These tables check bearing and tearout.
Note that edge distance, le, and bolt spacing, s, are measured to the centers of bolt holes, rather than the edges of the bolt holes.
Table 7-5 provides bearing strength at bolt holes based on edge distance.